## Slide 1: Model Driven Network Automation
Jason Belk, Network to Code

## Slide 2: Agenda
Introduction
  Data Encoding, Data Models, APIs, and Transport
Diving Deeper into RESTCONF
Exploring RESTCONF on IOS-XE with Postman

## Slide 3: Introduction
Notes: Introduction

## Slide 4
Unless we count the transition from telnet to SSH.
Network Operations & Management hasn’t changed for 20 years.
Why are we here?
Notes: Network operations and management hasn’t changed in 20 years
Unless you count SSH!

## Slide 5: From CLI to API
CLI is for humans
APIs are for machine to machine communication
APIs do not replace CLI
APIs can have a profound impact on operations
APIs facilitate operational efficiency
The industry is transitioning to an API first model
Notes: Industry is moving to API first model
- CLI Humans
- APIs
- Machine to machine communications
- Not CLI replacement
- Profound impact on operations by allowing automation
- Operational efficiency by allowing automation

## Slide 6: So many new terms…
…in this new world
NETCONF
RESTCONF
RESTful
XML
JSON
YAML
YANG
XSD
Postman
cURL
Python
Go
Ansible
SaltStack
Linux
Docker
Puppet
CoreOS
Mesosphere
gRPC
Model-Driven
API-first
Text Editors
IDEs
TABS vs. SPACES
Notes: So many new terms…. (Next Slide)

## Slide 7: So many new terms…
…in this new world
NETCONF
RESTCONF
RESTful
XML
JSON
YAML
YANG
XSD
Postman
cURL
Python
Go
Ansible
SaltStack
Linux
Docker
Puppet
CoreOS
Mesosphere
gRPC
Model-Driven
API-first
Text Editors
IDEs
TABS vs. SPACES
Notes: It is hard to put get a grasp on all of them, or even understand them all.

## Slide 8: Covering a subset of these today
Keep in mind the skills for the future network engineer are increasing
NETCONF
RESTCONF
RESTful
XML
JSON
YANG
Postman
Python
Linux
Model-Driven
Text Editors
TABS vs. SPACES
Notes: We cover a subset today

## Slide 9: Cisco IOS XE APIs Overview
Accept NETCONF and RESTCONF requests and communicates directly to configuration datastore(s).
Notes: IOS XE APIs Overview
- Service processes accept NETCONF and RESTCONF request and communicates with the configuration datastores.
- Application – Postman, Python, C, Java, Programs
- Transport – YANG data model defined XML or JSON (RESTCONF only)
- Network Device – Run server process (NETCONF and RESTCONF) which communicate with the devices management database.

## Slide 10: Objectives
Understand what data models are and why they’re important
Leave here knowing how to use Postman so you can explore any HTTP-based API
Become familiar with the basics of reading and executing Python scripts using IOS-XE APIs
Know enough to continue your IOS-XE API journey tomorrow
Realize you must understand the basics of programmability sooner than later
Understand you will not be an IOS-XE API expert in 4 hours 
Recognize learning takes time
Notes: Objectives
- Understand data model and why they are important
- Leave here knowing how to use Postman to explore REST APIs
- Basics of reading and executing Python scripts using IOS-EX APIs
- Continued exploration of the technology covered today
- You will become a programmer eventually, if you aren’t already
- Not an expert, more to learn
- Takes time to absorb all around APIs and functionality

## Slide 11: Breaking down Network APIs
Data Encoding
Data Models
Transport
Protocols
Notes: Data Encoding – The formatted structure which data is received and transmitted over the API
Data Models – Defines the structure of the data being encoded
Transport – SSH, HTTP, HTTPS, TLS, HTTP/2
Protocols – NETCONF, REST and RESTCONF

## Slide 12: Data Encoding
Who gets confused seeing “{}” or “</tag>” in code or text output?
Notes: What are all these confusing tags?

## Slide 13: Data Encoding
Who gets confused seeing “{}” or “</tag>” in code or text output?
Too bad? They are standard and take a little getting used to…
Notes: What are all these confusing tags?
To bad! Standard! Need to get use to it!

## Slide 14: Data Encoding
There needs to be structure behind what is communicated between systems
cisco#show run interface GigabitEthernet 1
Building configuration...
Current configuration : 146 bytes
!
interface GigabitEthernet1
vrf forwarding MANAGEMENT
ip address 10.0.0.151 255.255.255.0
negotiation auto
no mop enabled
no mop sysid
end
This is formatted text, not structured data
Notes: Data Encoding
Structure behind the data structure

## Slide 15: Data Encoding: JSON & XML
{
"Cisco-IOS-XE-native:GigabitEthernet": {
"name": "1",
"vrf": {
"forwarding": "MANAGEMENT"
},
"ip": {
"address": {
"primary": {
"address": "10.0.0.151",
"mask": "255.255.255.0"
}
}
},
"mop": {
"enabled": false,
"sysid": false
}
}
}
<GigabitEthernet>
<name>1</name>
<vrf>
<forwarding>MANAGEMENT</forwarding>
</vrf>
<ip>
<address>
<primary>
<address>10.0.0.151</address>
<mask>255.255.255.0</mask>
</primary>
</address>
</ip>
<mop>
<enabled>false</enabled>
<sysid>false</sysid>
</mop>
</GigabitEthernet>
JSON
XML
Notes: Data Encoding: JSON vs XML
- Same hierarchical structure based on YANG data model

## Slide 16: Data Encoding: JSON & XML
{
"Cisco-IOS-XE-native:GigabitEthernet": {
"name": "1",
"vrf": {
"forwarding": "MANAGEMENT"
},
"ip": {
"address": {
"primary": {
"address": "10.0.0.51",
"mask": "255.255.255.0"
}
}
},
"mop": {
"enabled": false,
"sysid": false
}
}
}
<GigabitEthernet>
<name>1</name>
<vrf>
<forwarding>MANAGEMENT</forwarding>
</vrf>
<ip>
<address>
<primary>
<address>10.0.0.151</address>
<mask>255.255.255.0</mask>
</primary>
</address>
</ip>
<mop>
<enabled>false</enabled>
<sysid>false</sysid>
</mop>
</GigabitEthernet>
JSON
XML
print response['Cisco-IOS-XE-native:GigabitEthernet']['ip']['address']['primary']['address']
10.0.0.151
print response.findall('.//{http://cisco.com/ns/yang/Cisco-IOS-XE-native}address')[1].text
10.0.0.151
Notes: Data Encoding: JSON vs XML
- Same hierarchical structure based on YANG data model

## Slide 17: Data Encoding
There needs to be structure behind what is communicated between systems
cisco#show run interface GigabitEthernet 1
Building configuration...
Current configuration : 146 bytes
!
interface GigabitEthernet1
vrf forwarding MANAGEMENT
ip address 10.0.0.151 255.255.255.0
negotiation auto
no mop enabled
no mop sysid
end
This is formatted text, not structured data
>>> for line in response.splitlines():
... if 'address' in line:
... print line.split('address')[1].split(' ')[1]
...
10.0.0.151
>>>
Other options exist. All use spacing, loops, or Regular Expressions.
Still very prone to error.
But, automation was/is still possible.
Notes: Data Encoding
- Structure behind the communication between systems
- Python example of parsing CLI output
- Prone to error
- Doesn’t adapt well to changed to CLI output
- Automation still possible despite these issues, but ultimately not recommended

## Slide 18: Data Encoding
Machines can easily parse XML and JSON. You can easily send an object that a machine understands.
Notes: Data Encoding
- Machines easily parse XML and JSON.

## Slide 19
We now know machines communicate using structured data.
What about the proper syntax and constraints of that data?
Notes: What about proper syntax and constraints on the data?

## Slide 20: Data Models
Data models describe a constrained set of data
Use well-defined parameters to standardize the representation of data
What are Data Models?
Notes: Data Models
What are they?
Describe a constrained set of date
Use defined parameters to standardized the format of the data

## Slide 21: Data Models
How do you describe a VLAN?
  VLAN ID
  VLAN name
  VLAN state
  …
Examples
Notes: Data Models - Examples
How do you describe a VLAN?
  ID
  Name
  State
  Etc…

## Slide 22: Data Models
How do you describe a VLAN?
  VLAN ID – integer between 1 and 4096 ?
  VLAN name – string between 1 and N characters ?
  VLAN state – enumeration of “down/up” or “shutdown/ no shutdown”
  …
  This is defining the constraints of the data– the Data Model for a VLAN.
Examples
Notes: Data Models - Examples
How do you describe a VLAN?
  ID - int 1 to 4096
  Name – str 1 to n chars
  State – enumeration (down|up) or (shutdown|no shutdown)
  Etc…

## Slide 23: YANG
It is a network-centric data modeling language defined in RFC 6020 specifically built for “network data”
Initially built for NETCONF
  Now also used by RESTCONF and can be used by any protocol
Models configuration and operational state data
Provides syntax and semantics
Notes: YANG
- Network centric data modeling language specifically for ”Network Data”
- Initially for NETCONF
- Models configuration and operational state data
- Provides syntax and semantics

## Slide 24: YANG
Sample YANG Module
Notes: YANG Sample

## Slide 25: YANG
Open and Native YANG Models
Notes: YANG Open and Native YANG Models
Industry Standard
  Policy definitions
  Basic System definitions
  Basic interface definitions
Cisco Common
  Common definitions across platforms
  Examples: OTV on IOS-XE and NX-OS
Cisco Platform Specific
  Unique to specfic platforms
  Examples: BGP extensions on IOS-XE

## Slide 26: Transport
The properly structured and encoded data still needs a way to get from point A to point B:
SSH
HTTP
HTTPS
TLS
HTTP/2
Notes: Transport
SSH
HTTP
HTTPS
TLS
HTTP/2

## Slide 27: APIs
NETCONF
Uses XML encoded data
Data that is transported is modeled either using YANG or XSD
NETCONF on IOS-XE uses XML data that adheres to YANG models
NETCONF protocol itself has network centric features (cover some of these later)
Transported over SSH
Two most common types of network APIs
REST (for network devices)
Uses XML or JSON encoded data
Modeled either using YANG, XSD, JSD, or custom modeling language
RESTCONF on IOS-XE uses XML/JSON data that adheres to YANG models
IOS-XE produces their REST API using data modeled from YANG  RESTCONF
Transported over HTTP/HTTPS
Notes: NETCONF
- XML data
- YANG Model Defined
- Network centric features
- SSH Transport
RESTCONF
- XML or JSON data
- YANG Model Defined
- REST API is defined from YANG model
- HTTP/HTTPS Transport

## Slide 28: Network Programmability Stack
Models
Encoding
Protocols
Bindings
Apps
NETCONF
gRPC
RESTCONF
XML
JSON
Software Development Kits (SDK) and libraries
YANG development kit (YDK)
Data Models
App1
App2
App3
SSH
HTTP(S)
Transport
TLS
REST
HTTP/2
Notes: NP Stack

## Slide 29: Diving Deeper into RESTCONF

## Slide 30
A little background on REST
Before RESTCONF…
Notes: Before RESTCONF some background on REST

## Slide 31: REST
If you understand how to work with a web browser, you understand REST.
Same HTTP Request Methods and Response Codes are used
HTTP GET
HTTP GET
JSON/XML
HTML
Notes: Understand how a web browser works, you understand REST
Same Request Methods and Response codes (HTTP Standards)

## Slide 32: REST
Create, Retrieve, Update and Delete (CRUD)
Create
Retrieve
Update
Delete
Notes: CRUD
Create
Retrieve
Update
Delete
Request Methods
POST
GET
PUT
DELETE

## Slide 33: REST
HTTP Verbs
GET
Retrieve / Read a resource
POST
Creates a new resource
PUT
Update/Replace a resource
DELETE
Removes a resource
PATCH
Update/Modify a resource
Notes: GET – Read resource
POST – Create a new resource
PUT – Update/Replace resource
PATCH – Update/Modify resource
DELETE – Remove resource

## Slide 34: REST
HTTP Verbs in the context of network devices
GET
Retrieve / Read a resource
POST
Creates a new resource
PUT
Update/Replace a resource
DELETE
Removes a resource
PATCH
Update/Modify a resource
create logical interface
replace full interface config with what’s in the body of request
update (append) interface config with what’s in the body of request
remove logical interface
show command
Notes: Network Device Examples
GET – Show commands
POST – Create logical interface
PUT – Replace full interface config
PATCH – update interface config
DELETE – Remove logical interface

## Slide 35: REST
Common HTTP Response Codes
Success (2xx) | Description
200 | Request Succeeded
201 | The request has been fulfilled; new resource created
204 | The server fulfilled request but does not return a body
Client Error (4xx) | Description
400 | Bad Request. Malformed Syntax
401 | Unauthorized
403 | Server understood request, but refuses to fulfill it.
404 | Resource not found given URI
Server Error (5xx) | Description
500 | Internal Server Error
501 | Not implemented
Notes: Common HTTP response codes
200 – Success
201 – Success resource created
204 – Success no response returned
500 – Internal Server Error
501 - Not Implemented - Wrong URL or structure defined in encoded data
400 – Bad Request – Invalid URL, invalid syntax data encoded, etc
401 – Unauthorized
403 – Forbidden
404 – URI not found

## Slide 36: Constructing an API Request
URL
HTTP Verb
  GET, POST, PATCH, PUT, DELETE
Body
  Used when making a configuration change. We’ll show a JSON Body soon.
Headers
  Define the structure of the data being sent and desired to be received.
  Are you using JSON or XML?
Authentication
  Your privileged level 15 credentials
Notes: Constructing API requests
- URL
- HTTP Verb (Request Method)
- Body – Encoded data structure
- Headers – Define data structure encoding, XML or JSON
- Authenication

## Slide 37: IOS-XE RESTCONF Request 1
URL - https://clus1/restconf/data/Cisco-IOS-XE-native:native/interface/GigabitEthernet=1
HTTP Verb
  GET
Body
  N/A
Headers
  Accept – application/yang-data+json
Authentication
  Your privileged level 15 credentials
Retrieving the GigE1 Configuration
Notes: Get GigE1 configuration RESTCONF request

## Slide 38: IOS-XE RESTCONF Response 1
{
"Cisco-IOS-XE-native:GigabitEthernet": {
"name": "1",
"vrf": {
"forwarding": "MANAGEMENT"
},
"ip": {
"address": {
"primary": {
"address": "10.0.0.151",
"mask": "255.255.255.0"
}
}
},
"mop": {
"enabled": false
},
"Cisco-IOS-XE-ethernet:negotiation": {
"auto": true
}
}
}
Retrieving the GigE1 Configuration
Notes: Returned JSON Encoded data struture

## Slide 39: IOS-XE RESTCONF Request 2
URL – https://clus1/restconf/data/Cisco-IOS-XE-native:native/interface/GigabitEthernet=2
HTTP Verb
  PATCH
Body
  
Headers
  Content-Type – application/yang-data+json
Authentication
  Your privileged level 15 credentials
Configuring GigE2
{
"Cisco-IOS-XE-native:GigabitEthernet": {
"ip": {
"address": {
"primary": {
"address": "10.2.0.151",
"mask": "255.255.255.0"
}
}
}
}
}
Notes: Configure GigE2 interface with RESTCONF
JSON encoded data

## Slide 40
So…REST vs. RESTCONF?
Notes: REST vs RESTCONF

## Slide 41: RESTCONF
It’s an implementation of a REST API
Model-driven API
Functional sub-set of NETCONF
Exposes YANG models via a REST API (URL)
Uses HTTP(S) as transport
Uses XML or JSON for encoding
Developed to use HTTP tools and programming libraries
What is it?
RESTCONF
HTTP(S)
NETCONF /YANG
Notes: RESTCONF
What is it?
Implementation of REST API
Model-driven API
Functional sub-set of NETCONF
Uses HTTP(S)
Data encoded in JSON or XML
Developed to use HTTP tools and programming libs

## Slide 42: RESTCONF
Almost identical to using any other RESTful API
Pay attention to the Accept and Content-Type Headers
  Typical RESTful APIs: application/json and application/xml
  RESTCONF: application/yang-data+json and application/yang-data+xml (others exist too)
Consuming the IOS-XE RESTCONF API
Notes: Consuming IOS-XE RESTCONF API
- Almost identical to using any RESTful API
- Make sure to understand Accept and Content-Type headers
- Typical
application/json
application/xml
- RESTCONF
application/vnd.yang.data+json
application/vnd.yang.data+xml

## Slide 43: Consuming RESTful APIs
Utilities and Tools
#!/usr/bin/env python
import requests
import json
from requests.auth import HTTPBasicAuth
requests.packages.urllib3.disable_warnings()
if __name__ == "__main__":
auth = HTTPBasicAuth('cisco', 'cisco')
headers = { 'Accept': 'application/yang-data+json'}
url = 'https://clus1/restconf/data/Cisco-IOS-XE-native:native/interface=GigabitEthernet/1'
response = requests.get(url, verify=False, headers=headers, auth=auth)
print response.text
$ curl -H "Accept:application/yang-data+json" –k -u cisco:cisco https://clus1/restconf/data/Cisco-IOS-XE-native:native/interface=GigabitEthernet/1
Postman
Chrome Application
requests
Python Module
cURL
Linux Command Line tool
Notes: Using RESTful APIs
Postman – Chrome Application or Standalone
Python – Request module
cURL – Linux command line tool

## Slide 44: What is Postman?
Notes: What is Postman?
Useful REST exploration and testing tool.

## Slide 45: Postman
Exploring HTTP-Based APIs
Notes: 1. History – every API call you make is saved in History. Since Postman is a Chrome application, History is shared between Postman (Chrome) sessions if you’re logged in different PCs.
2. Collections – you can create a collection of items from your History. This makes it possible to build out robust workflows and save them as a collection before you start development / coding.
3. HTTP Verb / Method – drop down for you to select the method required for the API: GET, POST, PATCH, PUT, DELETE, etc.
4. URL – this is where you enter the URL of your API endpoint
5. Authorization – your level 15 credentials will go here for IOS-XE (we’ll be using Basic Auth)
6. Headers – you will configure two headers here, Content-Type and Accept that’ll get sent in the HTTP Header
7. Send button that issues the API call to the device (API endpoint)